Design with an HDL
A Verilog Review
[Some slides adapted from A. Sprintson, M. Irwin, D. Paterson and others]

---
Verilog Overview
A Hardware Description Language (HDL) for describing & testing logic circuits.
  - text based way to talk about designs
  - easier to simulate before silicon
  - translate into silicon directly
    - Logic synthesis - automatic generation of lower-level logic circuit designs from high-level specifications

---
Why Verilog?
Why Verilog?
- Verilog: Similar to C, with some changes to account for time
- Widely used in industry
- VHDL is alternative; similar and can pick it up easily.
  - Verilog is simpler to learn!
- We will study only a simple subset of Verilog.

---
HDL to Gates
HDL to Gates
Simulation
Input values are applied to the circuit
Outputs checked for correctness
Millions of dollars saved by debugging in simulation instead of hardware
Synthesis
Transforms HDL code into a netlist describing the hardware (i.e., a list of gates and the wires connecting them)
IMPORTANT:
When describing circuits using an HDL, it is critical to think of the hardware the code should produce.

---
Verilog Overview
Verilog Overview
Verilog is a hardware description language
  - Although it looks like a general purpose language
- Describing circuits is not equivalent to programming
- Need to figure out the circuit first and then how to use Verilog to describe it.

---
Verilog Overview
Verilog Overview
Verilog description composed of modules:
module Name ( port list ) ;
Declarations and Statements;
endmodule
Modules can have instantiations of other modules or use primitives supplied by language

---
Verilog Overview
Verilog Overview
Verilog has 2 basic modes
1. Structural composition: describes the structure of the hardware components, including how ports of modules are connected together
  1. module contents are builtin gates (and, or, xor, not, nand, nor, xnor, buf) or other modules previously declared
2. Behavoral: describes what should be done in a module
  1. module contents are C-like assignment statements, loops

---
Basic gates: Inverter
Basic gates: Inverter
Truth Table
A	Y
0	1
1	0
Verilog – structural description
Input
Output
A
Y
Symbol
[Speaker Notes: credential: bring a computer die photo wafer : This can be an hidden slide· I just want to use this to do my own planning· I have rearranged Culler’s lecture slides slightly and add more slides· This covers everything he covers in his first lecture (and more) but may We will save the fun part, “ Levels of Organization,” at the end (so student can stay awake): I will show the internal stricture of the SS10/20· Notes to Patterson: You may want to edit the slides in your section or add extra slides to taylor your needs·]

---
Basic gates: Inverter
Basic gates: Inverter
Truth Table
A	Y
0	1
1	0
Verilog – structural description
module gate (Y, A);
input A;
output Y;
not inst1(Y,A);
endmodule
Input
Output
A
Y
Symbol
[Speaker Notes: credential: bring a computer die photo wafer : This can be an hidden slide· I just want to use this to do my own planning· I have rearranged Culler’s lecture slides slightly and add more slides· This covers everything he covers in his first lecture (and more) but may We will save the fun part, “ Levels of Organization,” at the end (so student can stay awake): I will show the internal stricture of the SS10/20· Notes to Patterson: You may want to edit the slides in your section or add extra slides to taylor your needs·]

---
The AND Gate
The AND Gate
A
B
Y

---
The AND Gate
The AND Gate
module gate (Y, A,B);
input A, B;
output Y;
and inst1(Y,A,B);
endmodule
A
B
Y

---
Example: Structural XOR (xor built-in,but..)
Example: Structural XOR (xor built-in,but..)
module xor(X, Y, Z);
input X, Y;
output Z;
wire notX, notY,
XnotY, YnotX;
not n0(notX, X);
not n1(notY, Y);
and a0(YnotX, notX, Y);
and a1(XnotY, X, notY);
or o0(Z, YnotX, XnotY);
endmodule
which “ports” input, output
Default is 1 bit wide data
“ports” connect components
Note: order of gates doesn’t matter,
since structure determines relationship

---
Adders in Verilog
Adders in Verilog
Half Adder
  - Add two single bit inputs
  - Output of a sum and a carry
- Full Adder
  - Add two single bit inputs with a carry in
  - Output of a sum and a carry out
- Larger Adders can be built from these single bit components (more on this to come)

---
Full – Adder in Verilog
Full – Adder in Verilog

---
Full – Adder in Verilog
Full – Adder in Verilog
module half_add (S, C, X, Y);
output S, C ;
input X, Y ;
xor x0(S, X, Y) ;
and a0(C, X, Y) ;
endmodule

---
Full – Adder in Verilog
Full – Adder in Verilog
module full_add (S, CO, A, B, CI) ;
output S, CO ;
input A, B, CI ;
wire N1, N2, N3;
half_add HA1 (N1, N2, A, B);
half_add HA2 (S, N3, N1, CI);
or P1 (CO, N3, N2);
endmodule
module half_add (S, C, X, Y);
output S, C ;
input X, Y ;
xor x0(S, X, Y) ;
and a0(C, X, Y) ;
endmodule

---
The AND Gate – behavioral Verilog
The AND Gate – behavioral Verilog
module gate (Y, A,B);
input A, B;
output Y;
assign Y=A & B;
endmodule
A
B
Y

---
Behavioral Verilog Example
Behavioral Verilog Example
Verilog:
module example(input a, b, c,
        output y);
  assign y = ~a & ~b & ~c | a & ~b & ~c | a & ~b & c;
endmodule
Synthesis: ?

---
Behavioral Verilog Example
Behavioral Verilog Example
Verilog:
module example(input a, b, c,
        output y);
  assign y = ~a & ~b & ~c | a & ~b & ~c | a & ~b & c;
endmodule
Synthesis:

---
Full – adder  - behavior model
Full – adder - behavior model
module fa_rtl (S, CO, A, B, CI) ;
output S, CO ;
input A, B, CI ;
assign S = A ^ B ^ CI;	//continuous assignment
assign CO = A & B | A & CI | B & CI; //continuous assignment
endmodule

---
Multiplexor – behavior model
Multiplexor – behavior model
A reg behaves like memory: holds its value until imperatively assigned otherwise
module mux(f, a, b, sel);
output f;
input a, b, sel;
reg f;
always @(a or b or sel)
  if (sel) f = b;
  else f = a;
endmodule
Sensitivity list contains signals whose change triggers the execution of the block
[Speaker Notes: credential: bring a computer die photo wafer : This can be an hidden slide. I just want to use this to do my own planning. I have rearranged Culler’s lecture slides slightly and add more slides. This covers everything he covers in his first lecture (and more) but may We will save the fun part, “ Levels of Organization,” at the end (so student can stay awake): I will show the internal stricture of the SS10/20. Notes to Patterson: You may want to edit the slides in your section or add extra slides to taylor your needs.]

---
Full – adder - Alternative behavior model
Full – adder - Alternative behavior model
Sensitivity list contains signals whose change triggers the execution of the block
module fa_bhv (S, CO, A, B, CI) ;
output S, CO ;
input A, B, CI ;
reg S, CO;	// required to “hold” values between events.
always@(A or B or CI)	//;
begin
   S = A ^ B ^ CI;	// procedural assignment
   CO = A & B | A & CI | B & CI;	// procedural assignment
end
endmodule

---
Example
Example
// Behavioral model of 4-bit Register:
// positive edge-triggered,
// synchronous active-high reset.
module reg4 (CLK,Q,D,RST);
input [3:0] D;
input CLK, RST;
output [3:0] Q;
reg [3:0] Q;
always @ (posedge CLK)
if (RST) Q <= 0; else Q <= D;
endmodule // reg4
On positive clock edge, either reset, or load with new value from D

---
Example
Example
initial
begin
CLK = 1'b0;
forever
#5 CLK = ~CLK;
end
...
- No built in clock in Verilog, so we need to specify one
- Clock CLK above alternates forever in 10 ns period:
  5 ns at 0, 5 ns at 1,
  5 ns at 0, 5 ns at 1, …
(Note: we assume a `timescale of 1ns/10ps here)

---
Example
Example
module add4 (S,A,B);
- a combinational logic block that forms the sum (S) of the two 4-bit binary numbers (A and B)
- Write the Verilog for this module in a behavioral style now
  - Assume this addition takes 4 ns

---
Example
Example
module add4 (S,A,B);
input [3:0] A, B;
output [3:0] S;
reg S;
always @(A or B)
#4 S = A + B;
endmodule
- a combinational logic block that forms the sum of the two 4-bit binary numbers, taking 4 ns
- Above is behavioral Verilog

---
Example
Example
// Accumulator
module acc (CLK,RST,IN,OUT);
input CLK,RST;
input [3:0] IN;
output [3:0] OUT;
wire [3:0] W0;
add4 myAdd (.S(W0), .A(IN), .B(OUT));
reg4 myReg (.CLK(CLK), .Q(OUT), .D(W0), .RST(RST));
endmodule // acc
This module uses prior modules, using wire to connect output of adder to input of register

---
Verilog Syntax
Verilog Syntax
Case sensitive
  - Example: reset and Reset are not the same signal.
- No names that start with numbers
  - Example: 2mux is an invalid name.
- Whitespace ignored
- Comments:
  - // single line comment
  - /* multiline
        comment */

---
Bitwise Operators
Bitwise Operators
module gates(input [3:0] a, b,
        output [3:0] y1, y2, y3, y4, y5);
   /* Five different two-input logic
      gates acting on 4 bit busses */
   assign y1 = a & b; // AND
   assign y2 = a | b; // OR
   assign y3 = a ^ b; // XOR
   assign y4 = ~(a & b); // NAND
   assign y5 = ~(a | b); // NOR
endmodule
// single line comment
/*…*/ multiline comment

---
Conditional Assignment
Conditional Assignment
module mux2(input [3:0] d0, d1,
        input s,
        output [3:0] y);
   assign y = s ? d1 : d0;
endmodule
? : is also called a ternary operator because it
        operates on 3 inputs: s, d1, and d0.

---
Internal Variables (wires)
Internal Variables (wires)
module fulladder(input a, b, cin, output s, cout);
  wire p, g; // internal nodes
  assign p = a ^ b;
  assign g = a & b;
  assign s = p ^ cin;
  assign cout = g | (p & cin);
endmodule

---
Numbers
Numbers
Format:	N'Bvalue
N = number of bits, B = base
N'B is optional but recommended (default is decimal)
Number	# Bits	Base	Decimal Equivalent	Stored
3’b101	3	binary	5	101
‘b11	unsized	binary	3	00…0011
8’b11	8	binary	3	00000011
8’b1010_1011	8	binary	171	10101011
3’d6	3	decimal	6	110
6’o42	6	octal	34	100010
8’hAB	8	hexadecimal	171	10101011
42	Unsized	decimal	42	00…0101010

---
Z: Floating Output
Z: Floating Output
Verilog:
module tristate(input [3:0] a,
        input en,
        output [3:0] y);
   assign y = en ? a : 4'bz;
endmodule
Synthesis:

---
Verilog big idea: Time
Verilog big idea: Time
Difference from normal prog. lang. is that time is part of the language
  - part of what trying to describe is when things occur, or how long things will take
- In both structural and behavoral Verilog, determine time with #n : event will take place in n time units
  - structural: not #2(notX, X) says notX does not change until time advances 2 ns
  - behavoral: Z = #2 A ^ B; says Z does not change until time advances 2 ns
  - Default unit is nanoseconds; can change

---
Time
Time
module example(input a, b, c,
        output y);
  wire ab, bb, cb, n1, n2, n3;
  assign #1 {ab, bb, cb} = ~{a, b, c};
  assign #2 n1 = ab & bb & cb;
  assign #2 n2 = a & bb & cb;
  assign #2 n3 = a & bb & c;
  assign #4 y = n1 | n2 | n3;
endmodule

---
Rising and Falling Edges and Verilog
Rising and Falling Edges and Verilog
Challenge of hardware is when do things change relative to clock?
  - Rising clock edge?
    (“positive edge triggered”)
  - Falling clock edge?
    (“negative edge triggered”)
  - When logical level is reached?
    (“level sensitive”)
- Verilog must support any “clocking methodology”
- Includes events “posedge”, “negedge” to say when clock edge occur, and “wait” statements for level

---
Always Statement
Always Statement
General Structure:
always @ (sensitivity list)
statement;
Whenever the event in the sensitivity list occurs, the statement is executed

---
Is it really correct?
Is it really correct?
Problem?
  - Where’s the register?
 The synthesis tool figures out that this is a combinational circuit. Therefore, it doesn’t need a register.
The register is there as an “artifact” of the descriptions — things on the left-hand side have to be registers.
module test (f, sel, b, c);
output	f;
input	sel, b, c;
reg	f;
always @ (sel or b or c)
if (sel == 1)
f = b;
else
f = c;
endmodule

---
Is it really correct?
Is it really correct?
Problem?
  - How does it figure out that this is combinational?
    - The output is only a function of the inputs (and not of previous values)
    - Anytime an input changes, the output is re-evauated
  - Think about the module as being a black box …
    - Could you tell that there is a register in there?
module test (f, sel, b, c);
output	f;
input	sel, b, c;
reg	f;
always @ (sel or b or c)
if (sel == 1)
f = b;
else
f = c;
endmodule

---
Resettable D Flip-Flop
Resettable D Flip-Flop
module flopr(input clk,
        input reset,
        input [3:0] d,
        output reg [3:0] q);
  // synchronous reset
  always @ (posedge clk)
    if (reset) q <= 4'b0;
    else q <= d;
endmodule

---
Resettable D Flip-Flop
Resettable D Flip-Flop
module flopr(input clk,
        input reset,
        input [3:0] d,
        output reg [3:0] q);
  // asynchronous reset
  ?
endmodule

---
Resettable D Flip-Flop
Resettable D Flip-Flop
module flopr(input clk,
        input reset,
        input [3:0] d,
        output reg [3:0] q);
  // asynchronous reset
  always @ (posedge clk, posedge reset)
    if (reset) q <= 4'b0;
    else q <= d;
endmodule

---
D Flip-Flop with Enable
D Flip-Flop with Enable
module flopren(input clk,
        input reset,
        input en,
        input [3:0] d,
        output reg [3:0] q);
  // asynchronous reset and enable
?
endmodule

---
D Flip-Flop with Enable
D Flip-Flop with Enable
module flopren(input clk,
        input reset,
        input en,
        input [3:0] d,
        output reg [3:0] q);
  // asynchronous reset and enable
  always @ (posedge clk, posedge reset)
    if (reset) q <= 4'b0;
    else if (en) q <= d;
endmodule

---
Other Behavioral Statements
Other Behavioral Statements
Statements that must be inside always statements:
if / else
case, casez
Reminder: Variables assigned in an always statement must be declared as reg (even if they’re not actually registered!)

---
Combinational Logic using always
Combinational Logic using always
// combinational logic using an always statement
module gates(input [3:0] a, b,
        output reg [3:0] y1, y2, y3, y4, y5);
  always @(*) // need begin/end because there is
    begin // more than one statement in always
      y1 = a & b; // AND
      y2 = a | b; // OR
      y3 = a ^ b; // XOR
      y4 = ~(a & b); // NAND
      y5 = ~(a | b); // NOR
    end
endmodule
This hardware could be described with assign statements using fewer lines of code, so it’s better to use assign statements in this case.

---
Combinational Logic using case
Combinational Logic using case
module sevenseg(input [3:0] data,
        output reg [6:0] segments);
  always @(*)
    case (data)
      // abc_defg
      0: segments = 7'b111_1110;
      1: segments = 7'b011_0000;
      2: segments = 7'b110_1101;
      3: segments = 7'b111_1001;
      4: segments = 7'b011_0011;
      5: segments = 7'b101_1011;
      6: segments = 7'b101_1111;
      7: segments = 7'b111_0000;
      8: segments = 7'b111_1111;
      9: segments = 7'b111_1011;
      default: segments = 7'b000_0000; // required
    endcase
endmodule

---
Combinational Logic using case
Combinational Logic using case
In order for a case statement to imply combinational logic, all possible input combinations must be described by the HDL.
Remember to use a default statement when necessary.

---
Combinational Logic using casez
Combinational Logic using casez
module priority_casez(input [3:0] a,
        output reg [3:0] y);
  always @(*)
    casez(a)
      4'b1???: y = 4'b1000; // ? = don’t care
      4'b01??: y = 4'b0100;
      4'b001?: y = 4'b0010;
      4'b0001: y = 4'b0001;
      default: y = 4'b0000;
   endcase
endmodule

---
Blocking vs. Nonblocking Assignments
Blocking vs. Nonblocking Assignments
<= is a “nonblocking assignment”
  - Occurs simultaneously with others
- = is a “blocking assignment”
  - Occurs in the order it appears in the file
// Good synchronizer using
// nonblocking assignments
module syncgood(input clk,
        input d,
        output reg q);
  reg n1;
  always @(posedge clk)
    begin
      n1 <= d; // nonblocking
      q <= n1; // nonblocking
    end
endmodule
// Bad synchronizer using
// blocking assignments
module syncbad(input clk,
        input d,
        output reg q);
  reg n1;
  always @(posedge clk)
    begin
      n1 = d; // blocking
      q = n1; // blocking
    end
endmodule

---
Rules for Signal Assignment
Rules for Signal Assignment
Use always @(posedge clk) and nonblocking assignments (<=) to model synchronous sequential logic
     always @ (posedge clk)
q <= d; // nonblocking
Use continuous assignments (assign …)to model simple combinational logic.
      assign y = a & b;
Do not make assignments to the same signal in more than one always statement or continuous assignment statement.

---
Finite State Machines (FSMs)
Finite State Machines (FSMs)
Three blocks:
next state logic
state register
output logic

---
FSM Example: Divide by 3
FSM Example: Divide by 3
The double circle indicates the reset state

---
FSM in Verilog
FSM in Verilog
module divideby3FSM (input clk,
        input reset,
        output q);
   reg [1:0] state, nextstate;
   parameter S0 = 2'b00;
   parameter S1 = 2'b01;
   parameter S2 = 2'b10;
// state register
   always @ (posedge clk, posedge reset)
      if (reset) state <= S0;
      else state <= nextstate;
 // next state logic
   always @ (*)
      case (state)
        S0: nextstate = S1;
        S1: nextstate = S2;
        S2: nextstate = S0;
        default: nextstate = S0;
      endcase
   // output logic
   assign q = (state == S0);
endmodule

---
Mealy FSM
Sequential logic
Combinational logic
Default

---
Mealy FSM

---
Moore FSM
Verilog?

---
Verilog code
Verilog code
Cascade chain of Flip-Flops
Bits travel on Clock edges
Serial in – Serial out, can also have parallel load / read

---
Testbenches
Testbenches
- HDL code written to test another HDL module, the device under test (dut), also called the unit under test (uut)
- Not synthesizeable
- Types of testbenches:
  - Simple testbench
  - Self-checking testbench
  - Self-checking testbench with testvectors

---
Testing your designs
Testing your designs
TESTBENCH is the final piece of hardware which
connect DESIGN with TEST so the inputs generated
go to the thing you want to test...
Your hardware
Another piece of hardware to generate interesting inputs

---
Example: Structural XOR
Example: Structural XOR
module xor(X, Y, Z);
input X, Y;
output Z;
wire notX, notY,
XnotY, YnotX;
not
  (notX, X),
  (notY, Y);
and
  (YnotX, notX, Y),
  (XnotY, X, notY);
or
  (Z, YnotX, XnotY);
endmodule

---
Testing Verilog
Testing Verilog
Create a test module that instantiates xor:
module testxor;
reg x, y, expected; wire z;
xor myxor(.x(x), .y(y), .z(z));
 /* add testing code */
endmodule
Syntax: declare registers, instantiate module.

---
Testing (continued)
Testing (continued)
Now we write code to try different inputs by assigning to registers:
…
initial
  begin
    x=0; y=0; expected=0;
#10 y=1; expected=1;
#10 x=1; y=0;
#10 y=1; expected=0;
  end

---
Testing continued
Testing continued
- Pound sign syntax (#10) indicates code should wait simulated time (10 nanoseconds in this case).
- Values of registers can be changed with assignment statements.
- So far we have the xor module and a testxor module that iterates over all the inputs. How do we see if it is correct?

---
Testing continued
Testing continued
- Use $monitor to watch some signals and see every time they change:
  …
  initial
  $monitor(“x=%b, y=%b, z=%b, exp=%b, time=%d”, x, y, z, expected, $time);
- Our code now iterates over all inputs and for each one: prints out the inputs, the gate output, and the expected output.
- $time is system function gives current time

---
Output
Output
x=0, y=0, z=0, exp=0, time=0
x=0, y=1, z=1, exp=1, time=10
x=1, y=0, z=1, exp=1, time=20
x=1, y=1, z=0, exp=0, time=30
Expected value matches actual value, so Verilog works

---
Example 1
Example 1
// Test bench for 2-input multiplexor.
// Tests all input combinations.
module testmux2;
reg [2:0] c;
wire f;
reg expected;
mux2 myMux (.select(c[2]), .in0(c[0]), .in1(c[1]), .out(f));
initial
begin
c = 3'b000; expected=1'b0; ...

---
Example 2
Example 2
… begin
c = 3'b000; expected=1'b0;
repeat(7)
begin
#10 c = c + 3'b001;
if (c[2]) expected=c[1];
else expected=c[0];
end
#10 $finish;
end

---
Example
Example
Write Verilog code to implement the following
function in hardware:
 y = bc + ab
Name the module sillyfunction

---
Example
Example
Write Verilog code to implement the following
function in hardware:
 y = bc + ab
Name the module sillyfunction
Verilog
module sillyfunction(input a, b, c,
        output y);
  assign y = ~b & ~c | a & ~b;
endmodule
How would you write a testbench for this code?

---
Simple Testbench
Simple Testbench
module testbench1();
  reg a, b, c;
  wire y;
  // instantiate device under test
  sillyfunction dut(a, b, c, y);
  // apply inputs one at a time
  initial begin
    a = 0; b = 0; c = 0; #10;
    c = 1; #10;
    b = 1; c = 0; #10;
    c = 1; #10;
    a = 1; b = 0; c = 0; #10;
    c = 1; #10;
    b = 1; c = 0; #10;
    c = 1; #10;
  end
endmodule

---
Self-checking Testbench
Self-checking Testbench
module testbench2();
  reg a, b, c;
  wire y;
  // instantiate device under test
  sillyfunction dut(a, b, c, y);
  // apply inputs one at a time
  // checking results
  initial begin
    a = 0; b = 0; c = 0; #10;
    if (y !== 1) $display("000 failed.");
    c = 1; #10;
    if (y !== 0) $display("001 failed.");
    b = 1; c = 0; #10;
    if (y !== 0) $display("010 failed.");
    c = 1; #10;
    if (y !== 0) $display("011 failed.");
    a = 1; b = 0; c = 0; #10;
    if (y !== 1) $display("100 failed.");
    c = 1; #10;
    if (y !== 1) $display("101 failed.");
    b = 1; c = 0; #10;
    if (y !== 0) $display("110 failed.");
    c = 1; #10;
    if (y !== 0) $display("111 failed.");
  end
endmodule

---
Testbench with Testvectors
Testbench with Testvectors
- Write testvector file: inputs and expected outputs
- Testbench:
  - Generate clock for assigning inputs, reading outputs
  - Read testvectors file into array
  - Assign inputs, expected outputs
  - Compare outputs to expected outputs and report errors

---
Testbench with Testvectors
Testbench with Testvectors
Testbench clock is used to assign inputs (on the rising edge) and compare outputs with expected outputs (on the falling edge).
The testbench clock may also be used as the clock source for synchronous sequential circuits.

---
Testvectors File
Testvectors File
File: example.tv – contains vectors of abc_yexpected
000_1
001_0
010_0
011_0
100_1
101_1
110_0
111_0

---
Testbench: 1. Generate Clock
Testbench: 1. Generate Clock
module testbench3();
  reg clk, reset;
  reg a, b, c, yexpected;
  wire y;
  reg [31:0] vectornum, errors; // bookkeeping variables
  reg [3:0] testvectors[10000:0]; // array of testvectors
  // instantiate device under test
  sillyfunction dut(a, b, c, y);
  // generate clock
  always // no sensitivity list, so it always executes
    begin
      clk = 1; #5; clk = 0; #5;
    end

---
2. Read Testvectors into Array
2. Read Testvectors into Array
 // at start of test, load vectors
 // and pulse reset
 initial
    begin
      $readmemb("example.tv", testvectors);
      vectornum = 0; errors = 0;
      reset = 1; #27; reset = 0;
    end
// Note: $readmemh reads testvector files written in
// hexadecimal

---
3. Assign Inputs and Expected Outputs
3. Assign Inputs and Expected Outputs
 // apply test vectors on rising edge of clk
  always @(posedge clk)
    begin
      #1; {a, b, c, yexpected} = testvectors[vectornum];
    end

---
4. Compare Outputs with Expected Outputs
4. Compare Outputs with Expected Outputs
// check results on falling edge of clk
   always @(negedge clk)
    if (~reset) begin // skip during reset
      if (y !== yexpected) begin
        $display("Error: inputs = %b", {a, b, c});
        $display(" outputs = %b (%b expected)",y,yexpected);
        errors = errors + 1;
      end
// Note: to print in hexadecimal, use %h. For example,
// $display(“Error: inputs = %h”, {a, b, c});

---
4. Compare Outputs with Expected Outputs
4. Compare Outputs with Expected Outputs
// increment array index and read next testvector
      vectornum = vectornum + 1;
      if (testvectors[vectornum] === 4'bx) begin
        $display("%d tests completed with %d errors",
        vectornum, errors);
        $finish;
      end
    end
endmodule
// Note: === and !== can compare values that are
// x or z.

---
What do we mean by “Synthesis”?
What do we mean by “Synthesis”?
Logic synthesis
  - A program that “designs” logic from abstract descriptions of the logic
  - takes constraints (e.g. size, speed)
  - uses a library (e.g. 3-input gates)
- How?
  - You write an “abstract” Verilog description of the logic
  - The synthesis tool provides alternative implementations
constraints
Verilog blah blah blah
synthesis
or …
library

---
In conclusion
In conclusion
- Verilog describes hardware in hierarchical fashion, either its structure or its behavior or both
- Time is explicit, unlike C or Java
- Time must be updated for variable change to take effect
- monitor print statement like a debugger; display, write, strobe more normal
- Modules activated simply by updates to variables, not explicit calls as in C or Java

---
In conclusion
In conclusion
- Verilog allows both structural and behavioral descriptions, helpful in testing
- Syntax a mixture of C (operators, for, while, if, print) and Ada (begin… end, case…endcase, module …endmodule)
- Some special features only in Hardware Description Languages
  - # time delay, initial, monitor
- Verilog can describe everything from single gate to full computer system; you get to design a simple processor

---
Review
Review
- Verilog easier to deal with when thought of as a hardware modeling tool, not as a prog lang.
- Verilog can describe everything from single gate to full computer system; you get to design a simple processor
- Using Verilog subset